## Slide 1: Conditional Processing
Computer Organization and Assembly Languages
with slides by Kip Irvine

## Slide 2: Announcements
Midterm exam: Room 103, 10:00am-12:00am next Thursday, open book, chapters 1-5.
Assignment #2 is online.

## Slide 3: Assignment #2 CRC32 checksum
unsigned int crc32(const char* data,
size_t length)
{
// standard polynomial in CRC32
const unsigned int POLY = 0xEDB88320;
// standard initial value in CRC32
unsigned int reminder = 0xFFFFFFFF;
for(size_t i = 0; i < length; i++){
// must be zero extended
reminder ^= (unsigned char)data[i];
for(size_t bit = 0; bit < 8; bit++)
if(reminder & 0x01)
reminder = (reminder >> 1) ^ POLY;
else
reminder >>= 1;
}
return reminder ^ 0xFFFFFFFF;
}

## Slide 4: Boolean and comparison instructions
CPU Status Flags
AND Instruction
OR Instruction
XOR Instruction
NOT Instruction
Applications
TEST Instruction
CMP Instruction

## Slide 5: Status flags - review
The Zero flag is set when the result of an operation equals zero.
The Carry flag is set when an instruction generates a result that is too large (or too small) for the destination operand.
The Sign flag is set if the destination operand is negative, and it is clear if the destination operand is positive.
The Overflow flag is set when an instruction generates an invalid signed result.
Less important:
  The Parity flag is set when an instruction generates an even number of 1 bits in the low byte of the destination operand.
  The Auxiliary Carry flag is set when an operation produces a carry out from bit 3 to bit 4

## Slide 6: NOT instruction
Performs a bitwise Boolean NOT operation on a single destination operand
Syntax: (no flag affected)
    NOT destination
Example:
  mov al, 11110000b
  not al
NOT

## Slide 7: AND instruction
Performs a bitwise Boolean AND operation between each pair of matching bits in two operands
Syntax: (O=0,C=0,SZP)
    AND destination, source
Example:
  mov al, 00111011b
  and al, 00001111b
AND
bit extraction

## Slide 8: OR instruction
Performs a bitwise Boolean OR operation between each pair of matching bits in two operands
Syntax: (O=0,C=0,SZP)
    OR destination, source
Example:
  mov dl, 00111011b
  or dl, 00001111b
OR

## Slide 9: XOR instruction
Performs a bitwise Boolean exclusive-OR operation between each pair of matching bits in two operands
Syntax: (O=0,C=0,SZP)
    XOR destination, source
Example:
  mov dl, 00111011b
  xor dl, 00001111b
XOR
XOR is a useful way to invert the bits in an operand and data encryption

## Slide 10: Applications (1 of 5)
mov al,'a' ; AL = 01100001b
and al,11011111b ; AL = 01000001b
Task: Convert the character in AL to upper case.
Solution: Use the AND instruction to clear bit 5.

## Slide 11: Applications (2 of 5)
mov al,6 ; AL = 00000110b
or al,00110000b ; AL = 00110110b
Task: Convert a binary decimal byte into its equivalent ASCII decimal digit.
Solution: Use the OR instruction to set bits 4 and 5.
The ASCII digit '6' = 00110110b

## Slide 12: Applications (3 of 5)
mov ax,40h ; BIOS segment
mov ds,ax
mov bx,17h ; keyboard flag byte
or BYTE PTR [bx],01000000b ; CapsLock on
Task: Turn on the keyboard CapsLock key
Solution: Use the OR instruction to set bit 6 in the keyboard flag byte at 0040:0017h in the BIOS data area.
This code only runs in Real-address mode, and it does not work under Windows NT, 2000, or XP.

## Slide 13: Applications (4 of 5)
mov ax,wordVal
and ax,1 ; low bit set?
jz EvenValue ; jump if Zero flag set
Task: Jump to a label if an integer is even.
Solution: AND the lowest bit with a 1. If the result is Zero, the number was even.

## Slide 14: Applications (5 of 5)
or al,al
jnz IsNotZero ; jump if not zero
Task: Jump to a label if the value in AL is not zero.
Solution: OR the byte with itself, then use the JNZ (jump if not zero) instruction.
ORing any number with itself does not change its value.

## Slide 15: TEST instruction
Performs a nondestructive AND operation between each pair of matching bits in two operands
No operands are modified, but the flags are affected.
Example: jump to a label if either bit 0 or bit 1 in AL is set.
test al,00000011b
jnz ValueFound
Example: jump to a label if neither bit 0 nor bit 1 in AL is set.
test al,00000011b
jz ValueNotFound

## Slide 16: CMP instruction (1 of 3)
Compares the destination operand to the source operand
  Nondestructive subtraction of source from destination (destination operand is not changed)
Syntax: (OSZCAP)
CMP destination, source
Example: destination == source
mov al,5
cmp al,5 ; Zero flag set
Example: destination < source
mov al,4
cmp al,5 ; Carry flag set

## Slide 17: CMP instruction (2 of 3)
Example: destination > source
mov al,6
cmp al,5 ; ZF = 0, CF = 0
(both the Zero and Carry flags are clear)
The comparisons shown so far were unsigned.

## Slide 18: CMP instruction (3 of 3)
Example: destination > source
mov al,5
cmp al,-2 ; Sign flag == Overflow flag
The comparisons shown here are performed with signed integers.
Example: destination < source
mov al,-1
cmp al,5 ; Sign flag != Overflow flag

## Slide 19: Setting and clearing individual flags
and al, 0 ; set Zero
or al, 1 ; clear Zero
or al, 80h ; set Sign
and al, 7Fh ; clear Sign
stc ; set Carry
clc ; clear Carry
mov al, 7Fh
inc al ; set Overflow
or eax, 0 ; clear Overflow

## Slide 20: Conditional jumps

## Slide 21: Conditional structures
There are no high-level logic structures such as if-then-else, in the IA-32 instruction set. But you can use combinations of comparisons and jumps to implement any logic structure.
First, an operation such as CMP, AND or SUB is executed to modified the CPU flags. Second, a conditional jump instruction tests the flags and change the execution flow accordingly.
CMP AL, 0
JZ L1
:
L1:

## Slide 22: Jcond instruction
A conditional jump instruction branches to a label when specific register or flag conditions are met
Jcond destination
Four groups: (some are the same)
based on specific flag values
based on equality between operands
based on comparisons of unsigned operands
based on comparisons of signed operands

## Slide 23: Jumps based on specific flags

## Slide 24: Jumps based on equality

## Slide 25: Jumps based on unsigned comparisons
＞≧＜≦

## Slide 26: Jumps based on signed comparisons

## Slide 27: Examples
  mov Large,bx
  cmp ax,bx
  jna Next
  mov Large,ax
Next:
Compare unsigned AX to BX, and copy the larger of the two into a variable named Large
  mov Small,ax
  cmp bx,ax
  jnl Next
  mov Small,bx
Next:
Compare signed AX to BX, and copy the smaller of the two into a variable named Small

## Slide 28: Examples
.date
intArray DWORD 7,9,3,4,6,1
.code
...
mov ebx, OFFSET intArray
mov ecx, LENGTHOF intArray
L1: test DWORD PTR [ebx], 1
jz found
add ebx, 4
loop L1
...
Find the first even number in an array of unsigned integers

## Slide 29: String encryption
encoder
message
(plain text)
unintelligible string
(cipher text)
key
encoder
message
(plain text)
key

## Slide 30: Encrypting a string
KEY = 239
.data
buffer BYTE BUFMAX DUP(0)
bufSize DWORD ?
.code
  mov ecx,bufSize ; loop counter
  mov esi,0 ; index 0 in buffer
L1:
  xor buffer[esi],KEY ; translate a byte
  inc esi ; point to next byte
  loop L1
Message: Attack at dawn.
Cipher text: «¢¢Äîä-Ä¢-ïÄÿü-Gs
Decrypted: Attack at dawn.

## Slide 31: Conditional loops

## Slide 32: LOOPZ and LOOPE
Syntax:
  LOOPE destination
  LOOPZ destination
Logic:
  ECX  ECX – 1
  if ECX > 0 and ZF=1, jump to destination
The destination label must be between -128 and +127 bytes from the location of the following instruction
Useful when scanning an array for the first element that meets some condition.

## Slide 33: LOOPNZ and LOOPNE
Syntax:
LOOPNZ destination
LOOPNE destination
Logic:
  ECX  ECX – 1;
  if ECX > 0 and ZF=0, jump to destination

## Slide 34: LOOPNZ example
.data
array SWORD -3,-6,-1,-10,10,30,40,4
sentinel SWORD 0
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
next:
  test WORD PTR [esi],8000h ; test sign bit
  pushfd ; push flags on stack
  add esi,TYPE array
  popfd ; pop flags from stack
  loopnz next ; continue loop
  jnz quit ; none found
  sub esi,TYPE array ; ESI points to value
quit:
The following code finds the first positive value in an array:

## Slide 35: Your turn
.data
array SWORD 50 DUP(?)
sentinel SWORD 0FFFFh
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
L1: cmp WORD PTR [esi],0 ; check for zero
quit:
Locate the first nonzero value in the array. If none is found, let ESI point to the sentinel value:

## Slide 36: Solution
.data
array SWORD 50 DUP(?)
sentinel SWORD 0FFFFh
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
L1: cmp WORD PTR [esi],0 ; check for zero
  pushfd ; push flags on stack
  add esi,TYPE array
  popfd ; pop flags from stack
  loope next ; continue loop
  jz quit ; none found
  sub esi,TYPE array ; ESI points to value
quit:

## Slide 37: Conditional structures

## Slide 38: Block-structured IF statements
Assembly language programmers can easily translate logical statements written in C++/Java into assembly language. For example:
  mov eax,op1
  cmp eax,op2
  jne L1
  mov X,1
  jmp L2
L1: mov X,2
L2:
if( op1 == op2 )
X = 1;
else
X = 2;

## Slide 39: Example
Implement the following pseudocode in assembly language. All values are unsigned:
  cmp ebx,ecx
  ja next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx )
{
eax = 5;
edx = 6;
}

## Slide 40: Example
Implement the following pseudocode in assembly language. All values are 32-bit signed integers:
  mov eax,var1
  cmp eax,var2
  jle L1
  mov var3,6
  mov var4,7
  jmp L2
L1: mov var3,10
L2:
if( var1 <= var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}

## Slide 41: Compound expression with AND
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is false, the second expression is skipped:
if (al > bl) AND (bl > cl)
X = 1;

## Slide 42: Compound expression with AND
cmp al,bl ; first expression...
ja L1
jmp next
L1:
cmp bl,cl ; second expression...
ja L2
jmp next
L2: ; both are true
mov X,1 ; set X to 1
next:
if (al > bl) AND (bl > cl)
X = 1;
This is one possible implementation . . .

## Slide 43: Compound expression with AND
cmp al,bl ; first expression...
jbe next ; quit if false
cmp bl,cl ; second expression...
jbe next ; quit if false
mov X,1 ; both are true
next:
if (al > bl) AND (bl > cl)
X = 1;
But the following implementation uses 29% less code by reversing the first relational operator. We allow the program to "fall through" to the second expression:

## Slide 44: Your turn . . .
Implement the following pseudocode in assembly language. All values are unsigned:
  cmp ebx,ecx
  ja next
  cmp ecx,edx
  jbe next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx
&& ecx > edx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)

## Slide 45: Compound Expression with OR
In the following example, if the first expression is true, the second expression is skipped:
if (al > bl) OR (bl > cl)
X = 1;

## Slide 46: Compound Expression with OR
cmp al,bl ; is AL > BL?
ja L1 ; yes
cmp bl,cl ; no: is BL > CL?
jbe next ; no: skip next statement
L1: mov X,1 ; set X to 1
next:
if (al > bl) OR (bl > cl)
X = 1;
We can use "fall-through" logic to keep the code as short as possible:

## Slide 47: WHILE Loops
while( eax < ebx)
eax = eax + 1;
A WHILE loop is really an IF statement followed by the body of the loop, followed by an unconditional jump to the top of the loop. Consider the following example:
_while:
cmp eax,ebx ; check loop condition
jae _endwhile ; false? exit loop
inc eax ; body of loop
jmp _while ; repeat the loop
_endwhile:

## Slide 48: Your turn . . .
_while: cmp ebx,val1 ; check loop condition
ja _endwhile ; false? exit loop
add ebx,5 ; body of loop
dec val1
jmp while ; repeat the loop
_endwhile:
while( ebx <= val1)
{
ebx = ebx + 5;
val1 = val1 - 1
}
Implement the following loop, using unsigned 32-bit integers:

## Slide 49: Example: IF statement nested in a loop
while(eax < ebx)
{
eax++;
if (ebx==ecx)
X=2;
else
X=3;
}
_while: cmp eax, ebx
jae _endwhile
inc eax
cmp ebx, ecx
jne _else
mov X, 2
jmp _while
_else: mov X, 3
jmp _while
_endwhile:

## Slide 50: Table-driven selection
Table-driven selection uses a table lookup to replace a multiway selection structure (switch-case statements in C)
Create a table containing lookup values and the offsets of labels or procedures
Use a loop to search the table
Suited to many comparisons

## Slide 51: Table-driven selection
.data
CaseTable BYTE 'A' ; lookup value
DWORD Process_A ; address of procedure
EntrySize = ($ - CaseTable)
BYTE 'B'
DWORD Process_B
BYTE 'C'
DWORD Process_C
BYTE 'D'
DWORD Process_D
NumberOfEntries = ($ - CaseTable) / EntrySize
Step 1: create a table containing lookup values and procedure offsets:

## Slide 52: Table-driven selection
mov ebx,OFFSET CaseTable ; point EBX to the table
mov ecx,NumberOfEntries ; loop counter
L1:cmp al,[ebx] ; match found?
jne L2 ; no: continue
call NEAR PTR [ebx + 1] ; yes: call the procedure
jmp L3 ; and exit the loop
L2:add ebx,EntrySize ; point to next entry
loop L1 ; repeat until ECX = 0
L3:
Step 2: Use a loop to search the table. When a match is found, we call the procedure offset stored in the current table entry:
required for procedure pointers

## Slide 53: Application: finite-state machines
A finite-state machine (FSM) is a graph structure that changes state based on some input. Also called a state-transition diagram.
We use a graph to represent an FSM, with squares or circles called nodes, and lines with arrows between the circles called edges (or arcs).
A FSM is a specific instance of a more general structure called a directed graph (or digraph).
Three basic states, represented by nodes:
  Start state
  Terminal state(s)
  Nonterminal state(s)

## Slide 54: Finite-state machines
Accepts any sequence of symbols that puts it into an accepting (final) state
Can be used to recognize, or validate a sequence of characters that is governed by language rules (called a regular expression)

## Slide 55: FSM Examples
FSM that recognizes strings beginning with 'x', followed by letters 'a'..'y', ending with 'z':
FSM that recognizes signed integers:

## Slide 56: Your turn . . .
Explain why the following FSM does not work as well for signed integers as the one shown on the previous slide:

## Slide 57: Implementing an FSM
StateA:
call Getnext ; read next char into AL
cmp al,'+‘ ; leading + sign?
je StateB ; go to State B
cmp al,'-‘ ; leading - sign?
je StateB ; go to State B
call IsDigit ; ZF = 1 if AL = digit
jz StateC ; go to State C
call DisplayErrorMsg ; invalid input found
jmp Quit
The following is code from State A in the Integer FSM:

## Slide 58: Isdigit
Isdigit PROC
cmp al,’0’
jb L1
cmp al,’9’
ja L1
test ax,0
L1: ret
Isdigit ENDP

## Slide 59: Your turn
StateB:
call Getnext ; read next char into AL
call Isdigit ; ZF = 1 if AL is a digit
jz StateC
call DisplayErrorMsg ; invalid input found
jmp Quit

## Slide 60: Implementing an FSM
StateC:
call Getnext ; read next char into AL
jz Quit ; quit if Enter pressed
call Isdigit ; ZF = 1 if AL is digit
jz StateC
cmp AL,ENTER_KEY ; Enter key pressed?
je Quit ; yes: quit
call DisplayErrorMsg ; no: invalid input
jmp Quit

## Slide 61: Finite-state machine example
[sign]integer.[integer][exponent]
sign → {+|-}
exponent → E[{+|-}]integer

## Slide 62: High-level directives
.IF eax > ebx
mov edx,1
.ELSE
mov edx,2
.ENDIF
.IF, .ELSE, .ELSEIF, and .ENDIF can be used to create block-structured IF statements.
Examples:
MASM generates "hidden" code for you, consisting of code labels, CMP and conditional jump instructions.
.IF eax > ebx && eax > ecx
mov edx,1
.ELSE
mov edx,2
.ENDIF

## Slide 63: Relational and logical operators

## Slide 64: MASM-generated Code
mov eax,6
cmp eax,val1
jbe @C0001
mov result,1
@C0001:
.data
val1 DWORD 5
result DWORD ?
.code
mov eax,6
.IF eax > val1
mov result,1
.ENDIF
Generated code:
MASM automatically generates an unsigned jump (JBE).

## Slide 65: .REPEAT directive
; Display integers 1 – 10:
mov eax,0
.REPEAT
inc eax
call WriteDec
call Crlf
.UNTIL eax == 10
Executes the loop body before testing the loop condition associated with the .UNTIL directive.
Example:

## Slide 66: .WHILE directive
; Display integers 1 – 10:
mov eax,0
.WHILE eax < 10
inc eax
call WriteDec
call Crlf
.ENDW
Tests the loop condition before executing the loop body The .ENDW directive marks the end of the loop.
Example: